## Slide 1
25.03.2022
TESA TWIN-SURF
Product presentation

## Slide 2: Key features
Compact, light et robust
90° probe orientation for transverse measurements
Store of the measured parameters
Wireless model available
Free software included for creating measurement reports

## Slide 3
Functions
Each measurement parameter can be activated / deactivated individually
Adjustable upper and lower tolerance for each parameter
Store of the measured parameters
Probe can be automatically returned to the starting position after each measurement
Menu available in 9 languages: English, French, German, italian, Spanish, Portuguese, Chinese, Japanese, Korean

## Slide 4
TESA TWIN-SURF 06930014 | TESA TWIN-SURF BT (integreated Bluetooth®) 06930015
TWIN-SURF portable roughness gauge | 
SB 51 probe | 
Main charger with EU and US charger adaptor | 
Roughness setting standard Ra = 2,97 µm | 
Adaptor for 8 mm diameter holder | 
Key to remove the probe protection | 
USB A-C cable | 
USB key including: User manual Measuring report Declaration of conformity TESA DATA-STUDIO software (basic version) | 
Scope of delivery

## Slide 5
TESA DATA-STUDIO | Basic version (no icence) | Premium version (with licence) Part N° 06960091
Parameters | 13 parameters | 51 parameters
Charts | Roughness R | R, P, Rk
Code management | Max 10 codes | Unlimited
Statistics | Max 10 mesurements | Unlimited
Functions
Display of roughness profiles
Storing of values
Save codes with custom measuring settings
Customized report in EXCEL or PDF with company logo
Compatible RUGOSURF 20
TESA DATA-STUDIO software

## Slide 6
TESA DATA-STUDIO software
Display of roughness profiles

## Slide 7
Store of values
TESA DATA-STUDIO software

## Slide 8
Save codes with custom measuring settings
TESA DATA-STUDIO software

## Slide 9
Customized report in EXCEL or PDF with company logo
TESA DATA-STUDIO software

## Slide 10
Statistics
TESA DATA-STUDIO software

## Slide 12: Transverse measurements SB51 probe

## Slide 13: Applications
Mesure transverales
Small bores measurements
SB31 probe

## Slide 14
Depth groove
measurements
SB121 probe

## Slide 15
Measurement
with 100 mm extension

## Slide 16
SB21 probe
SB31 probe
SB51 probe
SB121 probe
For groove of depth < 5 mm
For planes and holes
For small bores of Ø > 4 mm
Max depth 20 mm
For concave surfaces and for measuring at 90°
For groove of depth < 5 mm
For groove of depth < 20 mm
Probes

## Slide 18
Powered with a rechargeable battery, connector USB type C
Cable USB type C included
Automatic connection to the TWIN-SURF once paired (pairing through DATA-STUDIO)
Only compatible with TWIN-SURF BT
Printer

## Slide 19
Cable USB A-C
Part number 04760152
Extension 100 mm
Part number 06960096
Roughness setting standard, Ra = 2.97 µm
Part number 06960041
Power supply
Part number 04760150

## Slide 21
Standards | According to ISO 3274 - ISO 4287 - ISO 12085
Parameters | Parameters according to ISO 4287: Ra – Rq – Rt – Rz – Rc - Rmax - RSm - RPc Parameters according to ISO 12085: Pt – R – AR – Rx – PPc Additional parameters with software TESA DATA-STUDIO Premium version (with license): Parameters according to ISO 4287: Rp – Rv – Rsk – Rku – RΔq – RΔa – Rmr rel – Rδc – Rmr(c) Pa - Pq - Pp – Pv – Pt – Pc – RPc - R3z Psk – Pku - PSm- PΔq - Pmr rel – Pδc – Pmr (c) Rk – Rpk – Rvk - A1 – A2 - Mr1 – Mr2 Parameters according to ISO 12085: Rke – Rpke – Rvke - A1e – A2e – Mr1e – Mr2e
Max permissible error | 0,05 µm + (5 % R), R = Roughness in µm
Diamond-like stylus | R=2 µm, 90°
Specifications

## Slide 22
Specifications
Keyboard | Three-key tactile keyboard protected against dust particles and oil splashes IP67
Display | OLED display monochromatic 128x64 pixels
Dimensions | 160 x 34 x 34 mm (roughness gauge alone)
Poids | 200 g
Countries for which the wireless transmitter is approved (For TWIN-SURF BT 06930015) | EU, USA, Canada, Japan, China: Taiwan region only, South Korea, Brazil, Australia and New Zealand. For other countries, please contact us.

## Slide 23
Portable Roughness tester range
 | MEASURING RANGE |  | PARAMETERS | PROFILE TYPE |  |  | SKID |  | ADDITIONALS FEATURES
 | X axis | Z axis |  |  |  |  |  |  | 
 |  |  |  | R | P | W | with | without | 
RUGOSURF 20 06930013 | 16mm | 400µm | 13 |  |  |  |  |  | Compatible DATA-STUDIO
TWIN-SURF 06930014 | 16mm | 400µm | 13 |  |  |  |  |  | Transversal measurements Wireless model Compatible DATA-STUDIO Compatible portable printer
RUGOSURF 90G 06930012 | 50mm | 1000µm | 47 |  |  |  |  |  | Transversal measurements Compatible Meas. - STUDIO Profile Set available Special probes available

## Slide 24
Phase IN / OUT
RUGOSURF 10G
Part number 06930011
Orders available until End of year 2022
Replaced by 06930014
Software RUGOSOFT
Part number 06960034
Order until stock Ends
Replaced by 06960091

## Slide 25
Launch pack
Onboarding document
Product info
User manual
Pictures

## Slide 26
THANK YOU