## Slide 1
Quick Check - Bench Centers
Quick Check - Bench Centers
The Quick-Check center bench line comprises of a mix of standards parts from the well known multiflexprofile line , Mitutoyo indicator holders and dedicated parts. This keeps the prices affordable. The range starts out with 3 lengths with two variations each.
Indicator fine adjustment mechanism
Support of Dial- and Lever indicators with stems Ø 4 mm, Ø 8 mm and Ø 9,53 mm.
Fine adjustment of indicator position by 20° for smooth workpiece approach.
Indicator support bar L = 150mm
Holder bar H = 177 mm
Indicator Stand Features
20°
Main Unit Features

## Slide 2
Quick Check - Bench Centers Single-Rail Models
Quick Check - Bench Centers Single-Rail Models
Quick Check Bench Centers: Single-Rail Types
Quick Check Mono-Rail
Eccentricity check
One touch lever in/out support of shaft
Single-rail Types can be converted to Twin-Rail Types by adding the extension sets.
Sliders with additional indicator holders can be added for the positioning of multiple indicators.
Extend the height to 150mm by using the optional height extension set K551439.
Material | Distance between centers | Center height | Centre point angle | Indicator stand column height | Measuring arm length | Base plate | Load | weight
K551399 | 360 mm | 80 mm | 60° | 177 mm | 150 mm | 500 x 200 mm | 10 kg | 9,6 kg
K551425 | 600 mm | 80 mm | 60° | 177 mm | 150 mm | 740 x 200 mm | 10 kg | 12 kg
K551426 | 1.000 mm | 80 mm | 60° | 177 mm | 150 mm | 1.150 x 200 mm | 10 kg | 16,5 kg
Part No. | Range between centers | Length of Base | Width of Base | Height of Rod | Standard Height |  | With Height Extension* | 
 |  |  |  |  | Center Height | Tailstock Height | Center Height | Tailstock Height
Single-Rail | A | B | C | F | D | E | G | H
K551399 | 360 | 500 | 200 | 219,5 | 80 | 148 | 150 | 218
K551425 | 600 | 740 | 200 | 219,5 | 80 | 148 | 150 | 218
K551426 | 1000 | 1150 | 200 | 219,5 | 80 | 148 | 150 | 218
Dimensions: Single-Rail Types
*K551439 Height extension set
The Quick-Check center bench line comprises of a mix of standards parts from the well known multiflexprofile line , Mitutoyo indicator holders and dedicated parts. This keeps the prices affordable. The range starts out with 3 lengths with two variations each.

## Slide 3
Quick Check - Bench Centers Twin-Rail Models
Quick Check Bench Centers: Twin-Rail Types
Eccentricity check
One touch lever in/out support of shaft
Enables free positioning of the indicator along the part axis
Several sliders with indicator holders can be mounted optionally
Extend the height to 150mm by using the optional height extension set K551439.
Quick Check Twin-Rail
Part No. | Range between centers | Length of Base | Width of Base | Height of Rod | Standard Height |  | With Height Extension * | 
 |  |  |  |  | Center height | Tailstock Height | Center height | Tailstock Height
Twin-Rail | A | B | C | F | D | E | G | H
K551424 | 360 | 500 | 200 | 255 | 80 | 148 | 150 | 218
K551429 | 600 | 740 | 200 | 255 | 80 | 148 | 150 | 218
K551430 | 1000 | 1150 | 200 | 255 | 80 | 148 | 150 | 218
Material | Distance between centers | Center height | Centre point angle | Indicator stand column height | Measuring arm length | Base plate | Load | weight
K551424 | 360 mm | 80 mm | 60° | 177 mm | 150 mm | 500 x 200 mm | 10 kg | 11,4 kg
K551429 | 600 mm | 80 mm | 60° | 177 mm | 150 mm | 740 x 200 mm | 10 kg | 14,5 kg
K551430 | 1.000 mm | 80 mm | 60° | 177 mm | 150 mm | 1.150 x 200 mm | 10 kg | 20 kg
Quick Check - Bench Centers Twin-Rail Models
Dimensions: Twin-Rail Types
*K551439 Height extension set
The Quick-Check center bench line comprises of a mix of standards parts from the well known multiflexprofile line , Mitutoyo indicator holders and dedicated parts. This keeps the prices affordable. The range starts out with 3 lengths with two variations each.

## Slide 4
Quick Check - Bench Center Accessories
Quick Check - Bench Center Accessories
Twin-Rail Conversion Sets
Height extension set
The height of the Quick Check Bench Center can easily be extended from 80 mm to 150 mm, by adding the height extension set K551439. It comprises of two extension blocks and a 300 mm measuring arm rod, to easily reach the workpiece feature.
Part No. |  | Compatibility | Center height | Measuring arm length
K551439 | Height extension set for Quick Check 70 mm to increase center height from 80 mm to 150 mm | all Quick Check models | 150 mm | 300 mm
Scope of delivery
Part No. |  | Compatibility | Length A | Indicator stand | weight
K551422 | Indicator positioning rail set | K551399 | 500 mm | not included | 1,8 kg
K551428 | Indicator positioning rail set | K551429 | 740 mm | not included | 2,5 kg
K551427 | Indicator positioning rail set | K551426 | 1.150 mm | not included | 3,5 kg
Slider Unit and Indicator Stand
K551422
K551427
K551428
Scope of delivery
Part No. |  | Compatibility | Indicator stand | Indicator stand column height | Measuring arm length
K551432 | Slider unit for Quick Check | Quick Check twin- rail models | not included |  | 
K502620 | Clamp lever for slider components | K551432 |  |  | 
K916026 | Indicator stand for Quick Check slider | K551432 |  | 177 mm | 150 mm
02AZC390 | Extension rod for indicator holder 300 mm | K916026 |  |  | 300 mm
Part No. | Qty. | Part name
K580819 | 2 | Center raise block for Quick Check 70 mm 1 pc.
02AZC390 | 1 | 300 mm Extension rod for indicator holder
K916185 | 8 | Cylinder head screw M6
K551136 | 4 | Positioning bushing 10 mm multiflexprofile
K550561 | 8 | Spring washer Ø 6 mm
Total qty. | 23 | 
Part No. | Qty. | Part name
K551432 | 1 | Slider unit for Quick Check
K502620 | 1 | Clamp lever for slider components
K550633 | 1 | multiflexprofile rail 500 mm
K550110 | 4 | Cylinder head screw M6 x 20 mm
K550591 | 4 | Washer M6
K550561 | 4 | Spring washer Ø 6 mm
Total qty. | 15 | 
Part No. | Qty. | Part name
K551432 | 1 | Slider unit for Quick Check
K502620 | 1 | Clamp lever for slider components
K550833 | 1 | multiflexprofile rail 740 mm
K550563 | 4 | Cylinder head screw M6 25 mm
K550591 | 4 | Washer M6
K550561 | 4 | Spring washer Ø 6 mm
Total qty. | 15 | 
Part No. | Qty. | Part name
K551432 | 1 | Slider unit for Quick Check
K502620 | 1 | Clamp lever for slider components
K550822 | 1 | multiflexprofile rail 1.150 mm
K550563 | 4 | Cylinder head screw M6 25 mm
K550591 | 4 | Washer M6
K550561 | 4 | Spring washer Ø 6 mm
Total qty. | 15 |